Specifications.

The new BMW X3.

M40i.

|  |  |  | BMW X3 M40i |  |
| --- | --- | --- | --- | --- |
| Body |  |  |  |
| No of doors/seats |  |  | 5/5 |  |
| Length/width/height (unladen) | mm |  | 4716/1897/1676 |  |
| Wheelbase | mm |  | 2864 |  |
| Track, front/rear | mm |  | 1610/1594 |  |
| Ground clearance | mm |  | 204 |  |
| Turning circle | m |  | 12.1 |  |
| Fuel tank capacity | approx. ltr |  | 65 |  |
| Engine oil1) | ltr |  | 6.5 |  |
| Weight, unladen, to DIN/EU | kg |  | 1810/1885 |  |
| Max load to DIN | kg |  | 640 |  |
| Max permissible weight | kg |  | 2455 |  |
| Max axle load, front/rear | kg |  | 1190/1375 |  |
| Max trailer load, Braked (12%)/unbraked | kg |  | 2400/750 |  |
| Max roofload/max towbar download | kg |  | 100/100 |  |
| Luggage comp capacity | ltr |  | 550–1600 |  |
| Air resistance | Cd x A |  | 0.33 x 2.65 |  |
| Power Unit |
| Config/No of cyls/valves |  |  | in-line/6/4 |  |
| Engine technology |  | M Performance TwinPower Turbo technology: TwinScroll turbocharger, High Precision Direct Injection, VALVETRONIC fully variable valve control, Double-VANOS variable camshaft timing |
| Effective capacity | cc |  | 2998 |  |
| Stroke/bore | mm |  | 94.6/82.0 |  |
| Compression ratio | :1 |  | 11.0 |  |
| Fuel |  |  | min. RON 91 |  |
| Max output | kW/hp |  | 265/360 |  |
| at | rpm |  | 5500–6500 |  |
| Max torque | Nm/lb-ft |  | 500/369 |  |
| at | rpm |  | 1520–4800 |  |
| Electrical System |
| Battery/installation | Ah/– |  | 92/ luggage compartment |  |
| Driving Dynamics and Safety |
| Suspension, front |  | Aluminium double-joint spring strut axle |
| Suspension, rear |  | Five-link axle in lightweight steel construction |
| Brakes, front |  | Four-piston fixed-calliper disc brakes / vented |
| Brakes, rear |  | Double-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant, DSC networked with xDrive all-wheel-drive system, Hill Descent Control, Performance Control; optional: Dynamic Damper Control) |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt stopper, belt latch tensioner and belt force limiter at the front seats, crash sensors, tyre defect indicator |
| Steering |  | Electric Power Steering (EPS) est. available from 12/17, variable sport steering |
| Steering ratio, overall | :1 |  | 16.8 |  |
| Tyres, front/rear |  |  | 245/45 R20 103W XL 275/40 R20 106W XL |  |
| Rims, front/rear |  |  | 8.0J x 20 light alloy/ 9.5J x 20 light alloy |  |

|  |  |  | BMW X3 M40i |  |
| --- | --- | --- | --- | --- |
| Transmission |
| Type of transmission |  | 8-speed Sport Steptronic |
| Gear ratios I | :1 |  | 5.000 |  |
| II | :1 |  | 3.200 |  |
| III | :1 |  | 2.143 |  |
| IV | :1 |  | 1.720 |  |
| V | :1 |  | 1.314 |  |
| VI | :1 |  | 1.000 |  |
| VII | :1 |  | 0.822 |  |
| VIII | :1 |  | 0.640 |  |
| R | :1 |  | 3.456 |  |
| Final drive | :1 |  | 3.385 |  |
| Performance |
| Power-to-weight ratio | kg/kW |  | 6.8 |  |
| Output per litre | kW/ltr |  | 88.4 |  |
| 0–100 km/h | sec |  | 4.8 |  |
| In 5th gear 80–120 km/h | sec |  | -- |  |
| Top speed | km/h |  | 250 |  |
| BMW EfficientDynamics |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration with recuperation display, Electric Power Steering (EPS), Auto Start Stop function, ECO PRO mode, coasting function, intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-regulated oil pump, detachable a/c compressor, differential with optimised-warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption ECE2) |
| Urban | l/100 km |  | 11.1–10.8 |  |
| Extra-urban | l/100 km |  | 7.0–6.7 |  |
| Combined | l/100 km |  | 8.4–8.2 |  |
| CO2 | g/km |  | 193–188 |  |
| Emission rating |  |  | EU6 |  |

Specifications apply to ACEA markets/data relevant to homologation apply in part only to Germany (weight)

1) Oil change

2) Fuel consumption and CO2 emissions depend on the selected tyre format

The new BMW X3.

xDrive20d, xDrive30d.

|  |  | BMW X3 xDrive20d | BMW X3 xDrive30d |
| --- | --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 5/5 | 5/5 |
| Length/width/height (unladen) | mm | 4708/1891/1676 | 4708/1891/1676 |
| Wheelbase | mm | 2864 | 2864 |
| Track, front/rear | mm | 1620/1636 | 1620/1636 |
| Ground clearance | mm | 204 | 204 |
| Turning circle | m | 12.0 | 12.0 |
| Fuel tank capacity | app. ltr | 60 | 68 |
| Engine oil1) | ltr | 5.0 | 6,5 |
| Weight, unladen, to DIN/EU | kg | 1750/1825 | 1820/1895 |
| Max load to DIN | kg | 660 | 660 |
| Max permissible weight | kg | 2420 | 2500 |
| Max axle load, front/rear | kg | 1135/1395 | 1190/1415 |
| Max trailer load, Braked (12%)/unbraked | kg | 2400/750 | 2400/750 |
| Max roofload/max towbar download | kg | 100/100 | 100/100 |
| Luggage comp capacity | ltr | 550–1600 | 550–1600 |
| Air resistance | cd x A | 0.29 x 2.65 | 0.29 x 2.65 |
| Power Unit |  |  |
| Config/No of cyls/valves |  | in-line/4/4 | in-line/6/4 |
| Engine technology |  | BMW TwinPower Turbo technology: variable-geometry turbocharger, common rail direct injection |
| Effective capacity | cc | 1995 | 2993 |
| Stroke/bore | mm | 90.0/84.0 | 90.0/84.0 |
| Compression ratio | :1 | 16.5 | 16.5 |
| Fuel |  | diesel | diesel |
| Max output | kW/hp | 140/190 | 195/265 |
| at | rpm | 4000 | 4000 |
| Max torque | Nm/lb-ft | 400/295 | 620/457 |
| at | rpm | 1750–2500 | 2000–2500 |
| Electrical System |  |
| Battery/installation | Ah/– | 80/ luggage compartment | 92/ luggage compartment |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Aluminium double-joint spring strut axle |
| Suspension, rear |  | Five-link axle in lightweight construction |
| Brakes, front |  | Single-piston floating-calliper disc brakes / vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant, DSC networked with xDrive all-wheel-drive system, Hill Descent Control, Performance Control; optional: Dynamic Damper Control) |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt stopper, belt latch tensioner and belt force limiter at the front seats, crash sensors, tyre defect indicator |
| Steering |  | Electric Power Steering (EPS) est. available from 12/17, variable sport steering |
| Steering ratio, overall | :1 | 16.8 | 16.8 |
| Tyres, front/rear |  | 225/60 R18 104W XL | 225/60 R18 104W XL |
| Rims, front/rear |  | 7.0J x 18 light alloy | 7.0J x 18 light alloy |

|  |  | BMW X3 xDrive20d | BMW X3 xDrive30d |
| --- | --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | 8-speed Steptronic | 8-speed Steptronic |
| Gear ratios I | :1 | 5.000 | 5.000 |
| II | :1 | 3.200 | 3.200 |
| III | :1 | 2.143 | 2.143 |
| IV | :1 | 1.720 | 1.720 |
| V | :1 | 1.314 | 1.313 |
| VI | :1 | 1.000 | 1.000 |
| VII | :1 | 0.822 | 0.823 |
| VIII | :1 | 0.640 | 0.640 |
| R | :1 | 3.456 | 3.478 |
| Final drive | :1 | 3.231 | 2.813 |
| Performance |  |  |
| Power-to-weight ratio | kg/kW | 12.5 | 9.3 |
| Output per litre | kW/ltr | 70.2 | 65.2 |
| 0–100 km/h | sec | 8.0 | 5.8 |
| In 5th gear 80–120 km/h | sec | --- | --- |
| Top speed | km/h | 213 | 240 |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration with recuperation display, Electric Power Steering (EPS), Auto Start Stop function, ECO PRO mode, coasting function, intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-regulated oil pump, differential with optimised-warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption ECE2) |
| Urban | l/100 km | 5.2–4.9 | 6.6–6.3 |
| Extra-urban | l/100 km | 4.1–3.7 | 5.7–5.3 |
| Combined | l/100 km | 5.4–5.0 | 6.0–5.7 |
| CO2 | g/km | 142–132 | 158–149 |
| Emission rating |  | EU6 | EU6 |

Specifications apply to ACEA markets/data relevant to homologation apply in part only to Germany (weight)

1) Oil change

2) Fuel consumption and CO2 emissions depend on the selected tyre format

Output and torque diagrams
The new BMW X3.
M40i.

The new BMW X3.
xDrive 30d.

The new BMW X3.
xDrive 20d.

Exterior and interior dimensions.
The new BMW X3.